## Slide 1
ACADEMIC PRESENTATION · GROUP 17
AUTONOMOUS MOBILE MANIPULATION
Tennis-Bot
Vision-Guided Pick-and-Place on a Mobile Robot
A ROS 2 system integrating YOLOv5 detection, Nav2 autonomous navigation, SLAM mapping and Vosk voice control — built on the DJI RoboMaster EP and Jetson Orin NX.
GROUP 17
Presenters: Yanshan Wang, Wentian Li
Team Members: Yanshan Wang, Wenxin Xiao, Wentian Li, Guanhong Chen
Robotics & Embedded Systems Project
2026/5/27
ROS 2
YOLOv5
NAV2
VOSK
SLAM

## Slide 2
00
OVERVIEW
Presentation Agenda
01
Introduction
Project goal, motivation and target scenario on the tennis field.
02
Software & Hardware Stack
End-to-end system: vision, navigation, voice and embedded compute.
03
Code & Algorithm Flow
From static SLAM map to the SEARCHING → HOMING state machine.
PROJECT AT A GLANCE
5
State machine stages
4
Sensor modalities fused
100%
Autonomous on-court ops
ROS 2
Middleware foundation
02 / 21
GROUP 17 · TENNIS-BOT
AGENDA
Project Highlights
Project Team & Responsibilities
04
User Interface
Interaction design for operators and end users.
05
06
Highlighting the key innovative and distinctive features of our project design.
Clarifying the specific roles and contributions of each team member.

## Slide 3
01
INTRODUCTION
Project Overview & Objective
WHAT WE BUILT
Tennis-Bot is an autonomous mobile manipulator that collects scattered tennis balls on a court and deposits them into a designated bin — without any human intervention.
01
PERCEIVE
Detect tennis balls in real time using a YOLOv5 detector running on the Jetson Orin NX.
02
NAVIGATE
Use SLAM-built map + Nav2 stack for autonomous obstacle avoidance and goal-directed motion.
03
MANIPULATE
Drive a vision-servo loop on the DJI EP arm to grasp the ball and release it at the bin.
DJI RoboMaster EP + manipulator
GOAL Zero-touch ball collection on the court.
INTRODUCTION
03 / 21
GROUP 17 · TENNIS-BOT

## Slide 4
01
FIELD DEMONSTRATION
Project Overview & Objective - Autonomous Pick-and-Place Demonstration
Putting it all together — the robot autonomously scans the field, localizes against the SLAM map, and runs the full state machine end to end.
RViz2 — live AMCL particle cloud over the saved tennis_field map
Final Run · Live Demo
Full court Coverage area mapped
Auto Obstacle avoidance via Nav2
Vision-servo Grasp accuracy
Loop Repeats until court is empty
FIELD DEMO
04 / 21
GROUP 17 · TENNIS-BOT

## Slide 5
02
SOFTWARE & HARDWARE
System Architecture
PERCEPTION LAYER
CAM
USB Camera
RGB · 640×360 @ 30 fps
LDR
YDLidar X3
2D Lidar · 360° SLAM scan
ToF
ToF Sensor
IR distance · grab trigger
MIC
ReSpeaker 4-Mic
UAC1.0 · voice command
COMPUTE & SOFTWARE LAYER
GPU
Jetson Orin NX
ARM64 · CUDA acceleration
ROS
ROS 2 Humble
DDS · MultiThreadedExecutor
AI
YOLOv5 + Vosk
Detector · Chinese ASR
NAV
Nav2 + SLAM Toolbox
Planning · costmap · AMCL
ACTUATION LAYER
DRV
Mecanum Chassis
/cmd_vel · holonomic drive
ARM
Robotic Arm
MoveArm action · 2-DOF
GRP
Gripper
GripperControl action
UI
Status Overlay
OpenCV HUD on camera feed
DATA FLOW
Sensor input
Perception & decision
Actuator commands
ARCHITECTURE
05 / 21
GROUP 17 · TENNIS-BOT

## Slide 6
02
SOFTWARE & HARDWARE
Hardware Bill of Materials
Compact, ROS 2-native hardware stack — every component contributes a distinct sensing or actuation modality.
EDGE COMPUTE
Jetson Orin NX
ARM64 SoC with CUDA — runs YOLOv5, ROS 2 nodes, Nav2 and Vosk locally.
100 TOPS class
MOBILE PLATFORM
DJI RoboMaster EP
Mecanum-wheel chassis with built-in arm & gripper, accessed via robomaster_ros.
Holonomic drive
2D LIDAR
YDLidar X3
360° single-line scanner used by slam_toolbox for mapping and AMCL localization.
8 m range
VISION SENSOR
USB RGB Camera
Streams 640×360 frames via ROS 2 Image topic into YOLOv5 inference.
30 fps
PROXIMITY
ToF IR Sensor
Triggers the GRABBING transition once a ball is within ~13 cm of the gripper.
TRIGGER 0.13 m
VOICE INPUT
ReSpeaker 4-Mic
USB Audio Class 1.0 microphone array feeding Vosk Chinese ASR.
16 kHz mono
HARDWARE
06 / 21
GROUP 17 · TENNIS-BOT

## Slide 7
Software Stack
02
SOFTWARE & HARDWARE
LAYER
TECHNOLOGY
ROLE IN THE SYSTEM
Perception
YOLOv5 (PyTorch)
Real-time tennis ball detection on Jetson GPU
Vision Bridge
OpenCV + cv_bridge
Frame I/O, HUD overlay, debug visualization
Localization
SLAM Toolbox + AMCL
Build and localize against tennis_field.pgm
Navigation
Nav2 NavigateToPose
A* global planner + DWB local controller
Sensor Fusion
robot_localization
EKF fuses wheel odometry + IMU → /odom
Voice I/O
Vosk (small-cn-0.22)
Chinese keyword ASR — pause / resume
TF Tree
tf2_ros
Static base_link → laser_frame transform
Robot Driver
robomaster_ros
Chassis · arm · gripper · ToF action APIs
tennis_pick_nav2.py — imports
# ROS 2 core
import rclpy
from rclpy.node import Node
from rclpy.action import ActionClient
# Vision and sensor msgs
import cv2, torch, numpy as np
from sensor_msgs.msg import Image, Range
from cv_bridge import CvBridge
# Nav2 and RoboMaster actions
from nav2_msgs.action import NavigateToPose
from robomaster_msgs.action import \
MoveArm, GripperControl, Move
# Detector and voice (subprocess)
from models.common import DetectMultiBackend
import multiprocessing as mp # Vosk
SOFTWARE STACK
07 / 21
GROUP 17 · TENNIS-BOT

## Slide 8
03
Architecture & State FLOW
STRUCTURE OVERVIEW
08 / 21
GROUP 17 · TENNIS-BOT

## Slide 9
03
CODE FLOW
PIPELINE
Static Map
tennis_field.pgm
Bring-up
Lidar · EP · TF · EKF
Nav2 Stack
AMCL + planner + DWB
Vision Loop
YOLOv5 @ 30 fps
State Machine
5-state controller
Actuation
/cmd_vel + arm + grip
CONTROL STATE MACHINE
STATE 01
SEARCHING
scan for balls
STATE 02
ROTATING
align heading
STATE 03
GRABBING
approach + close
STATE 04
PLACING
Nav2 to bin · drop
STATE 05
HOMING
reset arm + gripper
loop back when HOMING completes
ASYNC INPUTS Vosk subprocess → pause/resume queue · ToF Range topic → grab trigger · AMCL pose → planner feedback
PIPELINE OVERVIEW
09 / 21
GROUP 17 · TENNIS-BOT

## Slide 10
03
CODE FLOW · 01
Step 1 — Building the Static Map
OFFLINE PHASE
Capture the court with SLAM Toolbox
Before any autonomous run we tele-operate the robot once around the tennis court. YDLidar X3 scans, slam_toolbox accumulates an occupancy grid in RViz, and nav2_map_server snapshots the result to tennis_field.pgm + .yaml — the ground truth that Nav2 will localize against later.
LAUNCH SEQUENCE
1
ydlidar_ros2_driver
2
robomaster_ros (EP)
3
static TF base_link→laser
4
EKF (robot_localization)
5
slam_toolbox async
6
RViz2 visualization
7
nav2_map_server save
tennis_field.pgm — saved occupancy grid
white = free · black = obstacle · gray = unknown
MAP BUILDING
10 / 21
GROUP 17 · TENNIS-BOT

## Slide 11
03
CODE FLOW · 02
State 1 — SEARCHING
INTENT
Drive YOLOv5 inference on every frame. When a tennis ball is confidently detected for several consecutive frames, lock onto the nearest one and hand off to ROTATING.
def run_searching(self):
def run_searching(self):
frame, detections = self._get_frame_and_detections()
high = [d for d in detections
if d['class_name'] == 'tennis'
and d['confidence'] > 0.7]
if high:
self.detect_count += 1
if self.detect_count >= DETECT_CONFIRM_FRAMES:
self.target_bbox = \
self._select_nearest_ball(high)['bbox']
return 'ROTATING' # transition
else:
self.lost_count += 1
if self.lost_count >= LOST_TRIGGER_FRAMES:
self._small_angle_search() # rotate
return 'SEARCHING'
Live HUD: STATE: SEARCHING — no detection above 0.7 confidence yet
DETECT_CONFIRM
3 frames
LOST_TRIGGER
5 frames
CONFIDENCE
> 0.7
STATE: SEARCHING
11 / 21
GROUP 17 · TENNIS-BOT

## Slide 12
03
CODE FLOW · 03
State 2 — ROTATING
Live HUD: STATE: ROTATING — chassis yawing until ball is image-centered
Proportional control
angle ∝ offset · 50° · damping
Oscillation guard
damping ×= 0.6 on sign flip
Timestamp gate
Only frames newer than last rotate
INTENT
Close a vision feedback loop: keep yawing the holonomic base until the ball's bounding-box center sits within ROTATE_TOLERANCE_PX of the image center.
run_rotating() — vision-servo align
for cnt in range(max_retry):
frame, detections = self._wait_fresh_frame(...)
nearest = self._select_nearest_ball(high)
x1, _, x2, _ = nearest['bbox']
offset = (x1 + x2)/2 - IMG_CENTER_X
if abs(offset) <= ROTATE_TOLERANCE_PX:
return 'GRABBING' # aligned
# adaptive damping to suppress oscillation
if last_offset is not None and \
last_offset * offset < 0:
damping *= 0.6
angle = (offset/(IMG_W/2)) * 50 * damping
self.chassis_move(0, 0, -angle, ...)
STATE: ROTATING
12 / 21
GROUP 17 · TENNIS-BOT

## Slide 13
03
CODE FLOW · 04
State 3 — GRABBING
INTENT
Open the gripper, drive forward while keeping the ball centered, and trip the grasp when ToF returns < TOF_TRIGGER_M. Close the gripper, then lift the arm for transport.
run_grabbing() — visual servo + ToF trigger
self.gripper_set(target='open', power=0.8)
twist = Twist()
while time.time() - start < 10:
# 1) ToF triggers the grasp
if self.latest_tof_m <= TOF_TRIGGER_M:
arrived = True; break
# 2) visual centering correction
offset = self._current_ball_offset()
twist.linear.x = CHASSIS_LINEAR_SPEED
twist.angular.z = -k * offset
self.cmd_vel_pub.publish(twist)
self.gripper_set(target='close', power=0.8)
self.arm_move(ARM_GRAB_LIFT_X, ARM_GRAB_LIFT_Z)
return 'PLACING'
Tennis ball framed by YOLOv5 — ToF closing in on trigger threshold
ToF Trigger
≤ 0.13 m
Linear Speed
0.30 m/s
Outcome
→ PLACING
STATE: GRABBING
13 / 21
GROUP 17 · TENNIS-BOT

## Slide 14
03
CODE FLOW · 05
State 4 — PLACING (Nav2 Autonomous Drive)
Robot autonomously navigating to the drop bin under Nav2
Action client
/navigate_to_pose
Global plan
A* / Dijkstra
Local plan
DWB + costmap
INTENT
Replaced the old open-loop trajectory with a Nav2 NavigateToPose call. Nav2 plans globally, dodges obstacles locally, AMCL refines the pose on arrival — release the ball, then reverse and rotate home.
run_placing() — Nav2 autonomous transit
def run_placing(self):
bx, by, byaw = self.box_pose
# delegate the full transit to Nav2
ok = self.navigate_to_pose_nav2(bx, by, byaw)
if not ok:
self.gripper_set(target='open', power=0.8)
return 'HOMING'
# arrived -> drop the ball
self.gripper_set(target='open', power=0.8)
self.chassis_move(-0.5, 0, 0, linear_speed=0.3)
self.chassis_move(0, 0, 180, angular_speed_deg=60)
return 'HOMING'
STATE: PLACING
14 / 21
GROUP 17 · TENNIS-BOT

## Slide 15
03
CODE FLOW · 06
State 5 — HOMING & Loop Back
INTENT
Reset the manipulator to its rest pose, re-open the gripper and clear the detection counters. Once HOMING completes, the state machine flows back to SEARCHING and the next ball is hunted.
run_homing() — reset and loop
def run_homing(self):
self.get_logger().info('>>> HOMING')
# bring the arm back to rest
self.arm_home()
self.gripper_set(target='open', power=0.8)
# clear vision counters for the next cycle
self.detect_count = 0
self.lost_count = 0
self.get_logger().info('>>> HOMING: done')
return 'SEARCHING' # loop
After release: arm retracts to ARM_HOME pose, gripper opens
CONTINUOUS OPERATION
HOMING → SEARCHING — the loop repeats until every ball on the court has been collected.
STATE: HOMING
15 / 21
GROUP 17 · TENNIS-BOT

## Slide 16
03
CODE FLOW · 07
Continuous Voice Monitoring — Async Safety Layer
INTENT
A voice-controlled override that runs in parallel with all 5 states. Vosk Chinese ASR listens continuously through the ReSpeaker array; the keyword 停止 (pause) instantly halts motion and cancels any active Nav2 goal, while 开始 (resume) releases the state machine to continue.
PROCESS ARCHITECTURE
VOICE WORKER PROCESS
ReSpeaker 4-Mic
→ sounddevice (float32)
→ Vosk (small-cn-0.22)
→ keyword match
mp.Queue
'pause' / 'resume'
MAIN ROS 2 NODE
VoiceController.dispatcher
→ _on_voice_pause()
· publish zero Twist ×5
· cancel Nav2 goal
EFFECT ON THE STATE MACHINE
Every motion routine calls _wait_if_paused() on entry — if a pause flag is set, the routine spins on a 100 ms idle until _pause_event is cleared. Result: every one of SEARCHING / ROTATING / GRABBING / PLACING / HOMING can be paused and resumed safely at any moment without breaking the loop.
Live terminal — Vosk hits '停止' → [PAUSE], then '开始' → [RESUME]
VOICE MONITORING
16 / 21
GROUP 17 · TENNIS-BOT

## Slide 17
03
CODE FLOW · 07
Voice Monitoring — Code Excerpt
KEY CALLBACKS
Two callbacks bridge the voice subprocess and the state machine; one method blocks any state when paused.
voice ←→ state-machine callbacks
def _on_voice_pause(self):
if self._pause_event.is_set():
return # idempotent
self.get_logger().warn(
'>>> [PAUSE] voice trigger')
self._pause_event.set()
# 1) zero-velocity stop
stop = Twist()
for _ in range(5):
self.cmd_vel_pub.publish(stop)
# 2) cancel active Nav2 goal
h = self._current_nav_handle
if h is not None:
h.cancel_goal_async()
def _on_voice_resume(self):
self._pause_event.clear()
blocking gate used by every motion routine
def _wait_if_paused(self, log_tag=''):
if not self._pause_event.is_set():
return False
self.get_logger().info(
f'>>> [PAUSE] {log_tag}...')
# idle until '开始' clears flag
while (self._pause_event.is_set()
and self.running and rclpy.ok()):
time.sleep(0.1)
self.get_logger().info(
'>>> [RESUME] continuing')
return True
# Vosk grammar (small-cn-0.22)
PAUSE_WORDS = {'停','停下','停止'}
RESUME_WORDS = {'开始','继续','走'}
Always-on Listens through every state
Instant cut-off 0-Twist × 5 + Nav2 cancel
Safe loop Resumes where it paused
VOICE MONITORING · CODE
17 / 21
GROUP 17 · TENNIS-BOT

## Slide 18
04
USER INTERFACE
Interaction Design — Operator Console
Design space reserved for the teammate-owned UI section: how an operator monitors, configures and steers the robot from a single screen.
01 · LIVE VIEW
Camera feed + YOLOv5 overlay, state badge and ToF distance bar.
02 · MAP & NAV
Real-time AMCL pose on tennis_field map; bin and goal markers.
UI DESIGN
18 / 21
GROUP 17 · TENNIS-BOT
Automatic ball-collecting robot console, with the left side displaying the real-time field map and ball position markers, and the right side integrating voice control, line-following mapping, system log recording, and field boundary scanning status.
Robot vision ball-picking interface, displaying the field scene and ball detection boxes in real time, with system logs updating continuously, and feedback on running speed and battery temperature at the bottom.

## Slide 19
05
HIGHLIGHTS
Project Highlights & Design Innovations
What sets Tennis-Bot apart from a textbook pick-and-place demo — design choices that pay off in the field.
PIPELINE
Closed-Loop Vision-to-Grasp Servo
Continuous bounding-box feedback drives both yaw alignment (ROTATING) and forward approach (GRABBING), with adaptive damping that suppresses oscillation on sign flip.
tolerance ≤ ROTATE_TOLERANCE_PX
PIPELINE
Nav2-Delegated Long-Range Transit
Replaced open-loop trajectories with the official Nav2 NavigateToPose action — global A* planning + DWB local control + AMCL localization on the saved tennis_field map.
A* / Dijkstra + DWB
PIPELINE
Multi-Target Nearest-First Selection
When several balls are detected simultaneously, the policy picks the largest bounding-box (≈ closest in 3-D) to minimize travel distance and avoid hunting between targets.
bbox-area ranking
FUNCTION
Continuous Voice Override
Vosk Chinese ASR in an isolated subprocess provides a true async safety channel — '停止' instantly cancels Nav2 goals & zeros /cmd_vel, '开始' resumes the exact same state.
停止 ⇄ 开始
FUNCTION
Heterogeneous Sensor Fusion
YOLOv5 vision + ToF IR proximity + 2D LiDAR + wheel odom + IMU are fused through an EKF and a state machine, each sensor only triggering the state that needs it.
4 modalities · 1 EKF
FUNCTION
On-Device Edge Compute
All perception, planning, ASR, and control run locally on a single Jetson Orin NX — no off-board GPU, no cloud, no network round-trips during a match.
100% on-device
HIGHLIGHTS
19 / 21
GROUP 17 · TENNIS-BOT

## Slide 20
06
TEAM
Project Team & Responsibilities
A balanced four-person team — each member owns one end-to-end module from algorithm design through code, hardware bring-up and field testing.
ROS 2 environment configuration on Jetson Orin NX
01
Yanshan Wang
System Design & Perception Lead
RESPONSIBILITIES
Overall framework and control flow design — defined the five-state machine
YOLOv5 tennis-ball detector training, fine-tuning, and Jetson Orin NX deployment
Vision pipeline and nearest-ball selection policy — OpenCV HUD overlay, frame I/O, bounding-box ranking, detection-confirm logic
02
Wenxin Xiao
Mapping & Navigation Lead
RESPONSIBILITIES
SLAM environment setup — YDLidar X3 driver, slam_toolbox, EKF (robot_localization), TF tree configuration
Nav2 stack configuration (planner, DWB, costmap, AMCL)
PLACING state — NavigateToPose action client integration
Indoor / outdoor mapping comparison experiments and failure-mode analysis
03
Wentian Li
HMI & UI Lead
RESPONSIBILITIES
Operator UI design and implementation — live camera + YOLO overlay panel, map & Nav goal panel, voice / control panel
On-screen status overlay — state badge, ToF distance bar, AMCL pose readout, voice ASR transcription stream
Robotic arm + gripper action clients (MoveArm, Gripper)
ToF IR sensor integration & grasp-trigger tuning
04
Guanhong Chen
Hardware & Voice Lead
RESPONSIBILITIES
Vosk + ReSpeaker voice-control subprocess design
Async pause/resume safety layer & _wait_if_paused gate
Operator UI mockups and on-screen status overlay
End-to-end system integration, packaging & field testing
SHARED EFFORT Map building, on-court testing, demo recording and final paper / slide preparation were carried out jointly by all four members.
TEAM
20 / 21
GROUP 17 · TENNIS-BOT
ROS 2 environment configuration on Jetson Orin NX
PPT slide design
Demo recording, screen capture, and final video post-production
Demo recording, screen capture, and final project report
Demo recording, screen capture, and final project report

## Slide 21
END OF PRESENTATION
Thank You
Questions & Discussion
Team Members: Yanshan Wang, Wenxin Xiao, Wentian Li, Guanhong Chen
Group 17 · Tennis-Bot — Robotics & Embedded Systems Project · 2026
ROS 2
YOLOv5
Nav2
SLAM
Vosk
Orin NX
DJI EP
ReSpeaker
GROUP 17